## Slide 1: Encoders and Decoders
Presentation on

## Slide 2: Encoders
Encoders is the combinational circuits that change the binary information into N output lines.
Encoder performs the reverse operation of the decoder.
An encoder has a number of input lines , only one of which is activated at a time.
It has 2n inputs.
It has n outputs.

## Slide 3: Types of encoders
Decimal to BCD encoder
Octal to binary encoder
Priority encoder
Hex to binary encoder

## Slide 4: Design 4 to 2 line Encoder
Inputs: There are total of four inputs i.e. I3,I2,I1,I0
Output: There are two outputs A1,A0
Block Diagram :
I0
I1 A0
I2
I3 A1

## Slide 5: Truth table
Inputs |  |  |  | outputs | 
I3 | I2 | I1 | I0 | A1 | A0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1

## Slide 6: Logical expression
A1=I3+I2
A0=I3+I1
Logical expression

## Slide 7: Design 8*3 Encoder
The 8*3 encoder is also known as octal to binary encoder.
In 8*3 line encoder:
8 inputs
3 outputs

## Slide 8: Block Diagram
I7
I6
I5 A2
I4
I3 A1
I2
I1 A0
I0

## Slide 9: Truth table
Inputs |  |  |  |  |  |  |  | Outputs |  | 
I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0 | A2 | A1 | A0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1

## Slide 10: Logical expression
A2=I4+I5+I6+I7
A1=I2+I3+I6+I7
A0=I7+I5+I3+I1
Logical Diagram

## Slide 11: Design decimal into BCD encoder(10:4)
The decimal to binary encoder usually consists of 10 input lines and 4 output.
Inputs= there are ten inputs.
Outputs=four outputs.
Block Diagram
8
Inputs outputs
Decimal to binary encoder

## Slide 12: Truth table
Inputs |  |  |  |  |  |  |  |  |  | Outputs |  |  | 
I9 | I8 | I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0 | A3 | A2 | A1 | A0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 13: Logical Diagram

## Slide 14: Priority Encoder 4 into 2 line priority encoder
In this priority encoder there are four inputs and two outputs A0 and A1
The I3 has high and I0 has low priority.
Block Diagram
Inputs Outputs
Priority
Encoder

## Slide 15: Truth table
inputs |  |  |  | Outputs |  | 
I3 | I2 | I1 | I0 | A1 | A0 | V
0 | 0 | 0 | 0 | * | * | 0
0 | 0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | * | 0 | 1 | 1
0 | 1 | * | * | 1 | 0 | 1
1 | * | * | * | 1 | 1 | 1

## Slide 16: Logical Expression
A1=I3+I2
A0=I3+I2’I1
Logical diagrams

## Slide 17: Decoder
It is combinational circuits, it change the binary information into 2n lines is known as decoders.
In decoders:
N inputs
2n outputs
Decoder enable input signal
Decoder performs the reverse operation of the encoder.

## Slide 18: Block Diagram
N Inputs 2noutputs
N to 2n decoders

## Slide 19: Design 2 into 4 line in Decoder
2 into 4 Decoder will consists of the following:
2 inputs
22 =4 outputs
1 Enable input signal(E)
Block Diagram
Inputs Outputs
2 into 4 Decoder

## Slide 20: Truth Table
Logical expression
X0=EA’B’ X1=EA’B
X2=EAB’ X3=EAB
Enable | Inputs |  | Outputs |  |  | 
E | A | B | X0 | X1 | X2 | X3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 21: Logical Diagram

## Slide 22: 3 into 8 decoder
3 Inputs
23=8 Inputs
1 Enable Input Signal
Block Diagram:
Inputs Outputs
3 into 8 Decoder

## Slide 23: Truth Table
Enable | Inputs |  |  | Outputs |  |  |  |  |  |  | 
E | A | B | C | X0 | X1 | X2 | X3 | X4 | X5 | X6 | X7
0 | d | d | d | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 24: Logical Expression
X0=A’B’C’ X1=A’B’C
X2=A’BC’ X3=A’BC
X4=AB’C’ X5=AB’C
X6=ABC’ X7=ABC
Logical Diagram

## Slide 25
Thank
you
Download ppt’s and handwritten notes
JP Web devolpers
Follow on instagram:-@jpwebdevelopers